## Slide 1: Supervised learning based hive protector
Presented by : Remi Goalard, Axel Pinel, Antonin Relandeau, Raphael Tessier, Sylvain Etienne, Jonathan Raecke, Pauline Dupuy
Tutors : Gwendoline Le Corre, Elodie Chanthery
Notes: Pauline

## Slide 2: Table of Contents
Introduction : Project’s context
Frequency Analysis of the hive’s noise
Hornet’s detection with an IA
Killing hornet device
Demonstrations of the prototype
Conclusion and discussion
Notes: Pauline

## Slide 3: Introduction : Project’s Context
Asian hornet a great danger to the bees
Current solutions present issues
Embedded constraints
  Limited power supply
  Easily transportable
Notes: Pauline

## Slide 4: Objectives of the Project
Objective 1 : Listen to the hive using microphone -> Detect danger
Objective 2 : Verifying Asian hornet presence on picture using AI
Objective 3 : Killing hornet with an automatic swatter
Side Objective : Low cost and easily reproducible system

## Slide 5: Project Management : 3 Teams for 3 Objectives
Agile method and 3 teams
  Frequency analysis
  Detection by an Artificial Intelligence
  Swatter system
Notes: Pauline

## Slide 6: Frequency Analysis of the Hive’s Noise Objective 1 : Method
Public beehive sound database : « To bee or not to bee »
→ check the sound produced by bees around hives during normal activity
Example
From 0 sec to 4.76 sec, there are bees around the microphone.
From 4.77 to 5.5 sec, there is not
Notes: Axel

## Slide 7: Frequency Analysis of the Hive’s Noise Objective 1 : Method
3 seconds-audio samples
+
Python program
Our database
Kaggle’s data
x 4780
x 4940
  Final database & program available on the GitHub page
  Possibility to use different parameters for the segmentation (time of the day, ...)
Notes: Axel

## Slide 8: Frequency Analysis of the Hive’s Noise Objective 1 : Method
Database processing:
  16 kHz resampling
Real Time processing
  Anti-aliasing filter
  Markov's window
  Reversed and Concatenated
Fast Fourier Transform
80 Hz – 120 Hz peak detection
Amplitude (in percentage of maximum)
Frequency (Hz)

## Slide 9: Frequency Analysis of the Hive’s Noise Objective 1 : Results
Peak detection parameters:
  Height
  Width
  Distance between peak
  Scoring based on true positive ratio
  Selection based on harmonic mean
  BEST SCORE : 53%

## Slide 10: Hornet’s Detection With an IA Objective 2
Start the IA when there is a noise alert
Detect hornet with a camera

## Slide 11: Hornet’s Detection with an IA Objective 2: Method
Dataset : 1500 images
Labialization with
  Hornet (Purple)
  Not Hornet (Red)
Model used
Train result analysis with
Notes: ~1500 annotated image on roboflow
image resize 640*640p
Label : ~2500 hornets, ~3000 not hornets
2200 images for training
310 validation
175 for testing
Yolov5small ; batch of 16; 50 iterations.

## Slide 12: Hornet’s Detection with an IA Objective 2: Results
Chart: Precision and Recall metrics evolution during the training program
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49
Precision | 0.23929 | 0.33264 | 0.43134 | 0.46123 | 0.51146 | 0.49375 | 0.59152 | 0.68629 | 0.58521 | 0.72824 | 0.73364 | 0.75058 | 0.6817 | 0.75971 | 0.69198 | 0.82254 | 0.75107 | 0.82984 | 0.8015 | 0.79811 | 0.82345 | 0.81717 | 0.79816 | 0.8024 | 0.83361 | 0.8365 | 0.84137 | 0.85206 | 0.80751 | 0.82489 | 0.84593 | 0.8274 | 0.8314 | 0.82858 | 0.81402 | 0.86889 | 0.87015 | 0.8719 | 0.84559 | 0.85232 | 0.85171 | 0.83417 | 0.83546 | 0.85316 | 0.85309 | 0.84982 | 0.87412 | 0.86042 | 0.86954 | 0.8575
Recall | 0.27942 | 0.40361 | 0.47527 | 0.38933 | 0.43417 | 0.44161 | 0.59469 | 0.66916 | 0.56111 | 0.65522 | 0.56834 | 0.7283 | 0.64926 | 0.69075 | 0.71006 | 0.75825 | 0.7213 | 0.73552 | 0.70832 | 0.7931 | 0.73464 | 0.76838 | 0.75071 | 0.75455 | 0.75032 | 0.73894 | 0.75977 | 0.75775 | 0.79348 | 0.79346 | 0.7821 | 0.78381 | 0.77261 | 0.76371 | 0.75207 | 0.75282 | 0.7413 | 0.75849 | 0.80589 | 0.78422 | 0.76368 | 0.77228 | 0.75636 | 0.77652 | 0.78638 | 0.76835 | 0.7771 | 0.77653 | 0.77254 | 0.7963
Notes: Precision : number of good true predicted element/ number of element predicted as true
Recall : indication of missed positive predictions nb of element well predict divide by nb real element
Precision 80%, recall 85%
No difference in loss between train et validation -> no overfitting

## Slide 13: Hornet’s Detection with an IA Objective 2: Results
Confusion matrix on the test dataset
Notes: TP FP
FN TN
Only 2% of error between hornets and bees

## Slide 14: Hornet’s Detection with an IA Objective 2: Results
Prediction on validation set
Prediction on debug sample
Notes: Implementation on jetson nano, detect almost every second
Threshold of 70% for validating detection, and counter to be sure
Objective : do not do useless or bee swatting
Possible amelioration : analyse position of the hornets to be suur that it is in the range of the swatter, (need to have a fixe package)

## Slide 15: Hornet’s Detection with an IA Objective 2: Results

## Slide 16: Hornet’s Detection with an IA Objective 2 : Package
Tinkercad 3D model: camera and Jetson microcomputer package
Up view
Under view

## Slide 17: Killing Device Objective 3: Design principles
Simplicity and robustness
Availability of components
Separation between trigger and loading mechanism
First mock-up
Prototype CAD model : perspective view

## Slide 18: Killing Device Objective 3: Design choices
Small teeth
Lightweight and material-efficient geometry
Use of adapters
  High flexibility & robustness to changes
Prototype CAD model : exploded view

## Slide 19: Killing Device Objective 3: Results
Automatic swatter device
Jetson nano -> gives strike command
12V solenoid -> lock the swatter
-> release the strike
12V motor -> reload the swatter

## Slide 20: Demonstration
We reused electronic components of others GEI projects
  Jetson Nano
  12VDC Solenoid
  12VDC motor and sailboat power circuit
  Global cost :
  220 € for Jetson Nano
  30-80€ for electronic components
  10€ for 3D-printed elements (without the printer)

## Slide 21: Demonstration
Entrance of a beehive to test our prototype

## Slide 22: Demonstrations of the Prototype
https://youtu.be/_yiAAEo7HgA

## Slide 23: Conclusion
Part of the project works :
  Detection of asian hornet’s image
  The swatter works
Some is still left to verify :
  Detection of asian hornet in real time
  The swatter kills the hornet
Some is still left to do :
  Make it embedded
  Make it affordable

## Slide 24: Files
Dataset available on https://universe.roboflow.com/pir/hornetv2/model/2
Program and 3D files available on https://github.com/raphaeltessier/Beehive-Protector

## Slide 25: Bibliography
Images :
Kaggle logo : https://www.kaggle.com/
Camera : https://www.flaticon.com/fr/icones-gratuites/cinema
Agile method : https://www.flaticon.com/fr/icones-gratuites/processus
ClearML : https://github.com/allegroai/clearml
Roboflow : https://images.app.goo.gl/hnUtVqaYBCQHdqez9
Yolov5 : https://images.app.goo.gl/11ayUJ2owt7ma3SNA
Hornet images: https://images.app.goo.gl/a6CeVaTw7weUXToT7; http://lyceedesandaines.fr/index.php/eco-lycee/357-un-specialiste-du-frelon-asiatique-conseille-le-pcs-abeilles ;
https://images.app.goo.gl/a5Nj1Xt8KzvnmiSVA
Demonstration : https://www.20minutes.fr/bordeaux/1217409-20130903-20130903-le-frelon-asiatique-toujours-present

## Slide 26: Participants
Students :
  Pinel Axel
  Relandeau Antonin
  Dupuy Pauline
  Tessier Raphael
  Goalard Rémi
  Étienne Sylvain
  Raecke Jonathan
Tutors :
  Chanthery Élodie
  Le Corre Gwendoline
  White Peeters Gemma